## Slide 1: Rapid Covert Physical Entry
Daniel Crowley

## Slide 2: Who am I?
Senior Security Engineer
Unhealthy preoccupation with unicorns
NCC Austin physical security guy

## Slide 3: Agenda
Lock Internals
Quick & Dirty Lock Manipulation
Sight-Reading Lock Difficulty
Lock Bypass
BONUS ROUND: Recommended Tooling

## Slide 4: Lock Internals

## Slide 5: Lock Internals
Basic Components
  Shackle
  Dog / Bolt
  Keyway
  Key

## Slide 6: Shackle
Restricts asset movement
  Target for destructive entry
  Directly interacts with asset to be locked
  Ultimately determines locked / unlocked state

## Slide 7: Dog / Bolt
Restricts shackle or asset
  Target for manipulation
  Movement should require key operation
    Often doesn’t (see picture)
    Sometimes can’t (single dial combination locks)

## Slide 8: Ball Bearing Dog

## Slide 9: Keyway

## Slide 10: Warded Locks
Key actuates dog
  Very simple mechanism
  Pieces of metal (wards) obstruct incorrect key movement
  Old design

## Slide 11: Multi-Wheel Combo Locks
Keyless design
  2D torus-shaped disks with notches on inside
  Toothed shackle / pawl

## Slide 12: Single-Dial Combo Locks
Safes and your gym locker
  VERY old design
  Series of interlocking disks with notches
  Correct disk rotation allows sidebar to fall into notches
  Sidebar recessed into notches allows shackle movement

## Slide 13: Lock Internals
Pin Tumbler Components
  Plug
  Bible
  Pin stacks
  Key and Driver pins

## Slide 14: Plug
Actuates locking dog
  Rotates inside lock
  Directly interacts with dog
  Usually the focus of lock hardening

## Slide 15: Pin Stacks
Restricts plug movement
  Each stack has:
    Key pin
    Driver pin
    Spring
    Master key pin (optional)
  Correct key lifts pin stacks to right height
    Usually 9 possible heights per pin

## Slide 16: Pin Stacks
Restricts plug movement
  Usually 4-6 pin stacks
  Top view shown here
    Not exactly accurate…

## Slide 17: Pin Stacks
Pin stack components
  Spring
  Driver pin
    Security pins
  Key pin

## Slide 18: Pin Stacks
Normal key operation
  Video shows removed plug and key pins

## Slide 19: Bible
Holds pin stacks
  Overly large bible may allow attacks
  Allows pins to retract from plug
  Springs push pins into plug

## Slide 20: Wafer Locks
Wafers, not pins
  Cheaper to produce
  Terrible quality

## Slide 21: Tubular Locks
Pin tumbler, but tubular
  Pins are pushed into lock
  Pins arranged in circle
  Same overall concept

## Slide 22: Agenda
Lock Internals
Quick & Dirty Lock Manipulation
Sight-Reading Lock Difficulty
Lock Bypass
BONUS ROUND: Recommended Tooling

## Slide 23: Q&D Lock manipulation

## Slide 24: Lock Raking
Apply torque to plug
Put pick in keyway
Go fscking nuts
???
OPEN!

## Slide 25: Lock Raking
Apply torque to plug
Put pick in keyway
Go fscking nuts
???
OPEN!

## Slide 26: Lock Raking
Apply torque to plug
Put pick in keyway
Go fscking nuts
???
OPEN!

## Slide 27: Lock Raking
Apply torque to plug
Put pick in keyway
Go fscking nuts
???
OPEN!

## Slide 28: Lock Raking
Apply torque to plug
Put pick in keyway
Go fscking nuts
???
OPEN!

## Slide 29: Lock Raking Haters
Taken condescendingly from Hacker News comments

## Slide 30: Lock Raking Haters
“If it’s stupid and it works, it ain’t stupid.”

## Slide 31: What just happened?
Remember the pin stacks
  Pins are not aligned perfectly

## Slide 32: What just happened?
Remember the pin stacks
  Pins are not aligned perfectly
  Manufacturing limitations
  Applying torque pinches pins from farthest left to farthest right
    Or right to left, if turning counter-clockwise

## Slide 33: What just happened?
SPP involves lifting each pinched (“binding”) pin
  Identify binding pin
  Lift pin to correct height
  Lifted pin held up by small ledge of rotated plug
  Repeat until all pins at correct height
Raking/jiggling/rocking is random movement and luck

## Slide 34: Lock Jiggling

## Slide 35: Direct Dog Manipulation
Move dog directly
  Via keyway

## Slide 36: Direct Dog Manipulation
Move dog directly
  Via keyway

## Slide 37: Direct Dog Manipulation
Move dog directly
  Via keyway
  Around shackle

## Slide 38: Making Padlock Shims
Drink your favorite canned beverage
Cut off bottom and top and make a sheet
Cut off a rectangle
Cut out a sine wave pattern
Fold down top, wrap prongs around
Curve shim

## Slide 39: Making Padlock Shims
Drink your favorite canned beverage
Cut off bottom and top and make a sheet
Cut off a small rectangle
Cut out a sine wave pattern
Fold down top, wrap prongs around
Curve shim

## Slide 40: Making Padlock Shims
Drink your favorite canned beverage
Cut off bottom and top and make a sheet
Cut off a rectangle
Cut out a sine wave pattern
Fold down top, wrap prongs around
Curve shim

## Slide 41: Making Padlock Shims
Drink your favorite canned beverage
Cut off bottom and top and make a sheet
Cut off a rectangle
Cut out a sine wave pattern
Fold down top, wrap prongs around
Curve shim

## Slide 42: Making Padlock Shims
Drink your favorite canned beverage
Cut off bottom and top and make a sheet
Cut off a rectangle
Cut out a sine wave pattern
Fold down top, wrap prongs around
Curve shim

## Slide 43: Bump Keys
Key blank cut to lowest bitting
  When “bumped” into lock, pops driver pin up
  Imagine pool or croquet balls
!!! May be illegal to own where you live !!!

## Slide 44: Bump Keys
Bump key operation
  Insert key into lock
  Pull key out one notch
  Apply slight torque
  Apply quick inward force on bump key

## Slide 45: Comb picking
Push pins completely out of plug
  Requires overly large bible
  Security pins don’t matter
  Works well with solid body padlocks

## Slide 46: Core / Bible shimming
Attack poor plug fit
  Slip shim between core and bible
  Pick each pin individually
  Situation-specific refinement on lock picking
Image taken from BosnianBill
https://youtube.com/user/bosnianbill

## Slide 47: Kinetic Attacks
Hit it
  But all special like
Not a euphemism for destructive entry
Actuates internal components using inertia
Photo from BosnianBill

## Slide 48: Impressioning
Create a key using the lock
  Uses “binding pin” principle of lock picking
  Binding pin creates scratches in key blank
  Takes time and patience for all but the super-elite

## Slide 49: Tubular Lock Impressioning
Far easier and quicker
  Effective at opening locks
  Can use fancy $85 tubular picks
  Can use a business card, scissors and tape

## Slide 50: Agenda
Lock Internals
Quick & Dirty Lock Manipulation
Sight-Reading Lock Difficulty
Lock Bypass
BONUS ROUND: Recommended Tooling

## Slide 51: Sight-Reading locks

## Slide 52: Lock Difficulties
Easy
Medium
Hard
NOPE
Quick to open with little training
Opens reliably with some training or special tools
Will not open quickly but given lots of time and training, could be done
If you have to ask, you can’t open it

## Slide 53: Caveat!
The locks mentioned are mostly US-centric

## Slide 54: Easy

## Slide 55: Wafer Locks
Wafer locks are cheap
Cheap manufacturing means easy picking
Very few high security wafer locks

## Slide 56: Master Locks
Easily picked
  Few notable exceptions
Lots of bypasses
  Master #175
  Master #14x
  Master #1,3,5
Model number etched near keyway

## Slide 57: Tubular Locks
Usually very easy
  A few are very hard!
Impressioning very effective, powerful, fast

## Slide 58: No-Name Locks
Tough to pick
  Shoddy construction
Almost always a bypass
  Shank it
  Shim it
  Rap it

## Slide 59: Tiny Locks
Hard to manufacture
  Requires compromises
Security features often missing
  Shim it
  Shank it
  Snip it
Image from Photobucket user 883xl

## Slide 60: Kwikset Classic
Super common door locks
No security pins
Easy to rake open
Bypasses for most Kwiksets

## Slide 61: Medium

## Slide 62: Kwikset SmartKey
Can be identified by hole to side of keyway
Hard to pick
Easy and cheap to decode, but takes time
Can be partially destroyed to directly actuate

## Slide 63: Schlage Classic
Annoying keyways
Mostly spool pins
With picking practice, opened quick enough

## Slide 64: Schlage Everest
An attempt at high security
  A failed attempt
Contains a single “check pin”
  Identical bitting across Everest locks
No security pins!

## Slide 65: Hard

## Slide 66: American Lock
Different types of security pins
Serrated pins are hell on earth

## Slide 67: SFIC
Interchangeable core
  One key opens lock
  Another key removes core
Normal picking yields success 1 in 2(pins-1)
Intentional overlifting attack

## Slide 68: Disc Detainer
Works like single-dial combo locks
Discs are rotated by angle-cut key
Difficult to manipulate in general
Most models are high-security

## Slide 69: NOPE

## Slide 70: Medeco
Awful keyways
Biaxial design
Security pins
Well-made
No known bypasses

## Slide 71: Schlage Primus
Six normal pins up top
Sidebar with six finger pins
  Must be lifted AND rotated like Medeco pins

## Slide 72: Lock bypass

## Slide 73: Loiding
The “credit card” trick
Directly actuate latch
Push or pull with
  Credit card
  Hotel room key
  Slim jim
  Mica shim
Latch guards
  Wedges and levers (rubber, air, crowbar)

## Slide 74: Under the Door
Under the door tool shown here
Exploits fire code
Exploits disability protections

## Slide 75: Disassembly
Sometimes you don’t need a key…
  …Just a screwdriver

## Slide 76: Environmental Failure
Sometimes you don’t need a key…
  …Just spatial skills

## Slide 77: Alternative entry point
Sometimes you don’t need a key…
  …Just common sense

## Slide 78: The End?
Daniel “unicornFurnace” Crowley
Daniel.Crowley@nccgroup.trust

## Slide 79: Recommended tooling

## Slide 80: Recommended Tooling

## Slide 81: Picks
TOOOL/Southern Specialties
Tremendous Twelve $30
PRO
  Great torque wrenches
  Falle hook
  Hooked diamond
CON
  Single-peak bogota
  Large half diamond

## Slide 82: Picks
Sparrows
Tuxedo $40
PRO
  Hooked diamond
  City rake
  Double-headed torque wrenches
  Low profile case
CON
  Cheap handles

## Slide 83: Picks
Peterson
Ken’s Pick Set $82
PRO
  Great materials
  Hard plastic handles
  Comes w/ shank tool
CON
  Price
  Too many hooks
  Peterson is a jerk

## Slide 84: Picks
Longhorn Lockpicking
Basic Pick Set $?
PRO
  Only what you need
  Solid steel handles
  Instant gratification
CON
  Nothing fancy
  One torque wrench

## Slide 85: Bypass Tools
Sparrows
Orion $25
PRO
  Flat and tubular torque wrenches
  Comb picks
  Shank
CON
  Awkward handles for comb picking and shanking

## Slide 86: Bypass Tools
Rift Recon
Under the Door tool 2.0 $50
PRO
  Folds up to backpack size
CON
  Wire-side handle gets painful with repeated use
  Really simple tool
    Make your own?

## Slide 87: Bypass Tools
BROCKHAGE
Stiff Air Wedge $30
PRO
  Stiff edge for easy insert
  Non-slip coating